- Manipulando bits

Obervação quanto aos pinos:

Pino	Nome	3,3V	5,0V		Pino	Nome	3,3V	5,0V
10	PA0	x			20	PB2	x	x
11	PA1	x			39	PB3	x	x
12	PA2	x			40	PB4	x	x
13	PA3	x			41	PB5	x
14	PA4	x			42	PB6	x	x
15	PA5	x			43	PB7	x	x
16	PA6	x			45	PB8	x	x
17	PA7	x			46	PB9	x	x
29	PA8	x	x		21	PB10	x	x
30	PA9	x	x		22	PB11	x	x
31	PA10	x	x		25	PB12	x	x
32	PA11	x	x		25	PB13	x	x
33	PA12	x	x		27	PB14	x	x
34	PA13	x	x		28	PB15	x	x
37	PA14	x	x		2	PC13	x
38	PA15	x	x		3	PC14	x
18	PB0	x			4	PC15	x
19	PB1	x

Na biblioteca main.h

#define EN1_Pin GPIO_PIN_0
#define EN1_GPIO_Port GPIOD
#define EN2_Pin GPIO_PIN_1
#define EN2_GPIO_Port GPIOD
#define EN4_Pin GPIO_PIN_14
#define EN4_GPIO_Port GPIOC

-- Setar um bit do port:

HAL_GPIO_WritePin(EN4_GPIO_Port, EN4_Pin, GPIO_PIN_SET);

-- Setar alguns bits do port:

HAL_GPIO_WritePin(GPIOD, EN1_Pin|EN2_Pin, GPIO_PIN_RESET);

-- Resetar um bit do port:

HAL_GPIO_WritePin(EN4_GPIO_Port, EN4_Pin, GPIO_PIN_RESET);

-- Resetar alguns bits do port:

HAL_GPIO_WritePin(GPIOA, D0_Pin|D1_Pin|D2_Pin|D3_Pin
        |D4_Pin|D5_Pin|D6_Pin|D7_Pin, GPIO_PIN_RESET);

- Lendo um bit do port:

uint8_t var;
var = HAL_GPIO_ReadPin(PP1_GPIO_Port, PP1_Pin);

-- Escrevendo de uma só vez no port:

GPIOA-> ODR = 0x0000; //Escreve 0000h em GPIOA
GPIOA-> ODR = 0b0000000000010000;

- Tipo de variáveis

Type	Size in bits	Natural alignment in bytes	Range of values
char	8	1 (byte-aligned)	0 to 255 (unsigned) by default. / –128 to 127 (signed) when compiled with --signed_chars.
signed char	8	1 (byte-aligned)	–128 to 127
unsigned char	8	1 (byte-aligned)	0 to 255
(signed) short	16	2 (halfword-aligned)	–32,768 to 32,767
unsigned short	16	2 (halfword-aligned)	0 to 65,535
(signed) int	32	4 (word-aligned)	–2,147,483,648 to 2,147,483,647
unsigned int	32	4 (word-aligned)	0 to 4,294,967,295
(signed) long	32	4 (word-aligned)	–2,147,483,648 to 2,147,483,647
unsigned long	32	4 (word-aligned)	0 to 4,294,967,295
(signed) long long	64	8 (doubleword-aligned)	–9,223,372,036,854,775,808 to 9,223,372,036,854,775,807
unsigned long long	64	8 (doubleword-aligned)	0 to 18,446,744,073,709,551,615
float	32	4 (word-aligned)	1.175494351e-38 to 3.40282347e+38 (normalized values)
double	64	8 (doubleword-aligned)	2.22507385850720138e-308 to 1.79769313486231571e+308 (normalized values)
long double	64	8 (doubleword-aligned)	2.22507385850720138e-308 to 1.79769313486231571e+308 (normalized values)
wchar_t	16 / 32	2 (halfword-aligned) / 4 (word-aligned)	0 to 65,535 by default. / 0 to 4,294,967,295 when compiled with --wchar32.
All pointers	32	4 (word-aligned)	Not applicable.
bool (C++ only)	8	1 (byte-aligned)	false or true
_Bool (C onlya)	8	1 (byte-aligned)	false or true

## Instruções:

if se verdadeiro
 if(HAL_GPIO_ReadPin(CHA_GPIO_Port, CHA_Pin))
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_SET);
 }
 else
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_RESET);
 }

if se falso
 if(!HAL_GPIO_ReadPin(CHA_GPIO_Port, CHA_Pin))
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_SET);
 }
 else
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_RESET);
 }

- Trabalhando com memória:

//Leitura da posição 0x08010000
uint8_t data;
data = *(uint8_t *)0x08010000;

- Manipulando registros

uint32_t pageAddress

pageAddress = 0x08010000;

FLASH->AR = pageAddress; //pageAddress recebe o endereço 08010000

FLASH->CR |= FLASH_CR_PER; //set bit PER of register FLASH_CR
FLASH->CR &= ~FLASH_CR_PER;//reset bit PER of register FLASH_CR

//Se o bit EOP do registro FLASH_SR for 1
if(FLASH->SR & FLASH_SR_EOP)
{
FLASH->SR &= ~FLASH_SR_EOP;
FLASH->CR &= ~FLASH_CR_PER;
return 1;
}

- Manipulando variáveis

number é a variável
x posição do bit

-- Setando um bit:

number |= 1 << x;

-- Resetando um bit:

number &= ~(1 << x);

- Alterando um bit:

number ^= 1 << x;

-- Testando um bit:

bit = (number >> x) & 1;

- Alterando o enésimo bit para x:

número ^ = (-x ^ número) & ( 1 << n);

-- Lendo de uma só vez no port:

uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx)
{
return ((uint16_t)GPIOx ->IDR);
}

Exemplo:

main:

/* USER CODE BEGIN PV */
uint16_t var;
/* USER CODE END PV */

...

/* USER CODE BEGIN PFP */
uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx);
/* USER CODE END PFP */

…

  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */
 var = GPIO_ReadInputData(GPIOB);
  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
//- Função para ler um port de 16 bits:
uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx)
{
return ((uint16_t)GPIOx ->IDR);
}

/* USER CODE END 4 */

- Função para ler um port de 16 bits:

uint16_t read_word(void)
{
   volatile uint16_t data = 0;
   data = (uint16_t)GPIOD->IDR & 0xffff;
   return data;
}

-- Função para escrever em um port de 16 bits:

void write_word(uint16_t cmd)
{
   //GPIOA->ODR = cmd & 0xffff;
   GPIOA->ODR = cmd;
}

- Função para ler dois port’s em 8 bits e guardar em uma variável de 16 bits:

uint16_t read_world_2(void)
{
    volatile uint16_t data = 0;
    data = (uint16_t)GPIOD->IDR & 0x00ff; //lsb
    data |= (uint16_t)GPIOA->IDR << 8 ; // msb
    return data;
}

- Função para escrever em dois port’s em 8 bits de uma variável de 16 bits:

void write_world_2(uint16_t cmd)
{
    GPIOD->ODR = cmd & 0x00ff; //lsb
    GPIOA->ODR = (GPIOA->ODR & 0x00ff) | (cmd >> 8); //msb
}

- Exemplo de utilização de definições

Exemplo utilizando o registro FLASH_CR (Flash control register) (PM0075)

Address offset: 0x10
Reset value: 0x0000 0080

Flash control register (FLASH_CR)
Address offset: 0x10
Reset value: 0x0000 0080

31	30	29	28	27	26	25	24	23	22	21	20	19	18	17	16
Reserved
15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
Reserved			EOPIE	Res.	ERRIE	OPTWR E	Res.	LOCK	STRT	OPTER	OPT / PG	Res.	MER	PER	PG
			rw		rw	rw		rw	rw	rw	rw		rw	rw	rw

Bits 31:13 Reserved, must be kept cleared.

Bit 12 EOPIE: End of operation interrupt enable
This bit enables the interrupt generation when the EOP bit in the	FLASH_SR register goes to 1.
0: Interrupt generation disabled
1: Interrupt generation enabled

Bit 11 Reserved, must be kept cleared

Bit 10 ERRIE: Error interrupt enable
This bit enables the interrupt generation on an FPEC error (when	PGERR / WRPRTERR are set in the FLASH_SR register).
0: Interrupt generation disabled
1: Interrupt generation enabled

Bit 9 OPTWRE: Option bytes write enable
When set, the option bytes can be programmed. This bit is set on	writing the correct key sequence to the FLASH_OPTKEYR register.
This bit can be reset by software

Bit 8 Reserved, must be kept cleared.

Bit 7 LOCK: Lock
Write to 1 only. When it is set, it indicates that the FPEC and	FLASH_CR are locked. This bit is reset by hardware after detecting	the unlock sequence. In the event of unsuccessful unlock operation,	this bit remains set until the next reset.

Bit 6 STRT: Start
This bit triggers an ERASE operation when set. This bit is set only	by software and reset when the BSY bit is reset.

Bit 5 OPTER: Option byte erase
Option byte erase chosen.

Bit 4 OPTPG: Option byte programming
Option byte programming chosen.

Bit 3 Reserved, must be kept cleared.

Bit 2 MER: Mass erase
Erase of all user pages chosen.

Bit 1 PER: Page erase
Page Erase chosen.

Bit 0 PG: Programming
Flash programming chosen.

Arquivo: definições.h

typedef struct
{
  __IO uint32_t ACR;
  __IO uint32_t KEYR;
  __IO uint32_t OPTKEYR;
  __IO uint32_t SR;
  __IO uint32_t CR;
  __IO uint32_t AR;
  __IO uint32_t RESERVED;
  __IO uint32_t OBR;
  __IO uint32_t WRPR;
} FLASH_TypeDef;

#define PERIPH_BASE 0x40000000UL
#define AHBPERIPH_BASE (PERIPH_BASE + 0x00020000UL)
#define FLASH_R_BASE (AHBPERIPH_BASE + 0x00002000UL)

#define FLASH ((FLASH_TypeDef *)FLASH_R_BASE)

#define FLASH_CR_PG_Pos (0U)
#define FLASH_CR_PG_Msk (0x1UL << FLASH_CR_PG_Pos) /*!< 0x00000001 */
#define FLASH_CR_PG FLASH_CR_PG_Msk /*!< Programming */

#define FLASH_CR_LOCK_Pos (7U)
#define FLASH_CR_LOCK_Msk (0x1UL << FLASH_CR_LOCK_Pos) /*!< 0x00000080 */
#define FLASH_CR_LOCK FLASH_CR_LOCK_Msk /*!< Lock */

Exemplo de utilização:

FLASH->CR &= ~FLASH_CR_PG; // ensure PG is low
FLASH->CR |= FLASH_CR_LOCK; // set the LOCK bit

while(FLASH->SR & FLASH_SR_BSY)
{
if(--timeout == 0)
{
return -1;
}
}

Exemplos de programas

- Exemplo 1

Escrevendo diretamente na porta A

main.c

/* USER CODE BEGIN PV */
uint16_t cmd;
/* USER CODE END PV */

...

  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */
 cmd=0x5555;
 write_word(cmd);
 HAL_Delay(1000);
 cmd=0xAAAA;
 write_word(cmd);
 HAL_Delay(1000);
  }
  /* USER CODE END 3 */

...

/* USER CODE BEGIN 4 */
void write_word(uint16_t cmd)
{
   GPIOA->ODR = cmd;
}
/* USER CODE END 4 */

- Exemplo 2

Deslocamento de bits para a esquerda

main.c

/* USER CODE BEGIN PV */
uint8_t x=0;
uint16_t cmd=0;
/* USER CODE END PV */

…

  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */

 cmd |= 1 << x;
 write_word(cmd);
 HAL_Delay(100);

 cmd &= ~(1 << x);
 write_word(cmd);
 HAL_Delay(100);

 x++;

 if(x == 10)
 {
 x=0;
 }

  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
void write_word(uint16_t cmd)
{
   GPIOA->ODR = cmd;
}
/* USER CODE END 4 */

- Exemplo 3

Deslocamento de bits para a direita

main.c

/* USER CODE BEGIN PV */
int x=9;
uint16_t cmd=0;
/* USER CODE END PV */

…

  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */

 cmd |= 1 << x;
 write_word(cmd);
 HAL_Delay(100);

 cmd &= ~(1 << x);
 write_word(cmd);
 HAL_Delay(100);

 x--;

 if(x < 10)
 {
 x=9;
 }

  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
void write_word(uint16_t cmd)
{
   GPIOA->ODR = cmd;
}
/* USER CODE END 4 */

- Exemplo 4

Deslocamento de bits para a direita e para a esquerda

main.c

/* USER CODE BEGIN PV */
uint8_t x1=5, x2=4, y=0;
uint16_t cmd=0;
/* USER CODE END PV */

…

  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */

 cmd |= 1 << x1;
 cmd |= 1 << x2;
 write_word(cmd);
 HAL_Delay(100);

 cmd &= ~(1 << x1);
 cmd &= ~(1 << x2);
 write_word(cmd);
 HAL_Delay(100);

 x1++;
 x2--;
 y++;

 if(y == 5)
 {
 y=0;
 x1=5;
 x2=4;
 }

  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
void write_word(uint16_t cmd)
{
   GPIOA->ODR = cmd;
}
/* USER CODE END 4 */

- Exemplo 5

Lendo um port inteiro de 16 bits, armazenando em uma variável e testando o 10 bit. Caso seja 1, liga o bit L0. Caso seja 0, desliga o bit L0

main.h

#define L0_Pin GPIO_PIN_0
#define L0_GPIO_Port GPIOA

main.c

/* USER CODE BEGIN PV */
uint8_t x;
uint16_t var;
/* USER CODE END PV */

…

/* USER CODE BEGIN PFP */
uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx);
/* USER CODE END PFP */

…

  /* Infinite loop */
  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */
 var = GPIO_ReadInputData(GPIOB);

 x = 10;
 if((var >> x) & 1)
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_SET);
 }
 else
 {
 HAL_GPIO_WritePin(L0_GPIO_Port, L0_Pin, GPIO_PIN_RESET);
 }
  }
  /* USER CODE END 3 */

…

/* USER CODE BEGIN 4 */
//- Função para ler um port de 16 bits:
uint16_t GPIO_ReadInputData(GPIO_TypeDef* GPIOx)
{
return ((uint16_t)GPIOx ->IDR);
}

/* USER CODE END 4 */